Main Battle Tank T-90

The Russian T-90 Main Battle tank is one of the best tanks in the world.

Its main armament is 125-mm gun. It is adapted for firing AT-11 antitank guided missiles with laser guidance. Its firing range is 4000 m.

The turret carries the NSVT 12.7 mm antiaircraft machine gun with the vertical stabilization. The T-90 is capable of killing most of the enemy tanks and helicopters located outside the reach range. A digital ballistic computer and laser range-finder incorporated in the fire control system makes it possible to destroy targets with high accuracy.

The MBT-90 is protected by the optical electronic system “Shtora” which can create jamming in the optical range for control lines of aviation bombs, aviation guided missiles. Searchlights are constantly active and radiate a coded infra-red signal preventing from accurate guidance of enemy antitank guided missile.

The tank turret mounts 12 grenade launchers for laying aerosol screens.

Besides, the T-90 tank is fitted with a laser.

Specifications:

- Crew-3

- Height-3.6 m

- Weight-42 t

- Width-2.2 m

- Maximum road speed-70 km per hour

- Distance range-.650 km

Can surmount such obstacles as:

- A hill-0.8 m

- Water depth- 11.6 m

На главную страницу   ©Докучаева Ирина Вениаминовна, 2007-2008